## Slide 1: GSoap & ONVIF
Cathy Chiang
9/27/2010

## Slide 2
Start
Accept socket
Close
Http Library
Check state
Release conn
close
release
Create conn
Create thread
failed
Socket send data
Cgi, html handler
socket Non-
Blocking Read
Gsoap handler
failed
No(Original path)
Check URI
“/onvif/device_service”
Or “onvif/services”
Socket Recv data
(use flag of MSG_PEEK)
Yes
Delivered socket fd to gsoap
HttpAuth
Free Soap

## Slide 3: Add API for Http Library
int soap_handler(int socket)
{
struct soap *soap = NULL;
if (gSrvConf.conf.misc.onvif_state == DISABLE)
return ERR;
if(!(soap = soap_new())) return ERR;
soap->socket = socket;
soap_serve(soap);
soap_destroy(soap);
soap_end(soap);
soap_free(soap);
return OK;
}

## Slide 4: Discovery (Discoverable)
Client
Device
Hello / multicast
Bye / multicast
Probe / multicast
ProbeMatch / unicast
Probe / unicast
ProbeMatch / unicast
AddScopes, SetScope, RemoveScopes
Hello / multicast
System Reboot
onvif via Http
Conditional:
1. ONVIF Service enable
2. DeviceType== “NetworkVideoTransmitter”

## Slide 5
Main code start
Services start up
DiscoveryMulticast_Hello
Server Config Ready
OnvifDiscoveryThreadCreate
TV Standard Changed
DecideVideoSourceVideoEncoder
Save Config Command
OnvifConfBin2File
Reboot
ThreadDiscoveryUnicastClose
DiscoveryMulticast_Bye
Firmware Server

## Slide 6: ONVIF initiation
Onvif.conf
(/etc/config/)
Start
Onvif.conf exist ?
Generate default ONVIF config
no
Convert onvif.conf
to onvif config
yes
read

## Slide 7: Default ONVIF Config definition
Scopes [maximum: 10]: GetScopes, SetScopes, AddScopes, RemoveScopes
  onvif://www.onvif.org/type/video_encoder : Fixed
  onvif://www.onvif.org/type/audio_encoder :Fixed
  onvif://www.onvif.org/hardware/ :Fixed
  onvif://www.onvif.org/name/$MODEL_NAME :Fixed
  onvif://www.onvif.org/location/ : Configurable
VideoSources [maximum: 2]: GetVideoSources
  [0]: Token: “0”, FrameRate: maximum frame rate
  [1]: reserved
VideoSources Configuration [maximum: 2]: GetVideoSourceConfigurations, SetVideoSourceConfigurations, …
  [0]: Token: “0”, name: “user0”, VideoSourceIdx: 0, Resolution: max. resolution group
  [1]: reserved
VideoEncoder Configuration [maximum: 8]: GetVideoEncoderConfigurations, SetVideoEncoderConfigurations, …
  [0]: Token: “HighResolution_MPEG4”, name: “highresolution mpeg4”, width=max. width, height: max.height Encoding: MPEG4, Quality: 80, frameratelimit:0, bitratelimit:0, encodinginterval:0, multicast: non-implemented
  [1]: Token: “VGA_MPEG4”, name: “VGA mpeg4”, width=640, height: 480 Encoding: MPEG4, Quality: 80, frameratelimit:0, bitratelimit:0, encodinginterval:0, multicast: non-implemented
  [2]: Token: “HighResolution_JPEG”, name: “highresolution JPEG”, width=max. width, height: max.height Encoding: JPEG, Quality: 80, frameratelimit:0, bitratelimit:0, encodinginterval:0, multicast: non-implemented
  [3]: Token: “VGA_JPEG”, name: “VGA JPEG”, width=640, height: 480 Encoding: JPEG, Quality: 80, frameratelimit:0, bitratelimit:0, encodinginterval:0, multicast: non-implemented
  [4]:Token: “0”, name: “user0”, width=640, height: 480 Encoding: MPEG4, Quality: 80, frameratelimit:0, bitratelimit:0, encodinginterval:0, multicast: non-implemented
  [5]: Token: “1”, name: “user1”, width=640, height: 480 Encoding: MPEG4, Quality: 80, frameratelimit:0, bitratelimit:0, encodinginterval:0, multicast: non-implemented
  [6-7] reserved
Media Profiles [maximum: 6]: GetProfiles, GetProfile, CreateProfile
  [0]: Token: “HighResolution_MPEG4”, name:”HighResolution mpeg4”, videosourceIdx: 0, videoEncoderIdx: 0
  [1]: Token: “VGA _MPEG4”, name:”VGA mpeg4”, videosourceIdx: 0, videoEncoderIdx: 1
  [2]: Token: “HighResolution_JPEG”, name:”HighResolution jpeg”, videosourceIdx: 0, videoEncoderIdx: 2
  [3]: Token: “VGA _JPEG”, name:” VGA jpeg”, videosourceIdx: 0, videoEncoderIdx: 3

## Slide 8: /etc/config/Onvif.conf
DISCOVERY_MODE='0' /* 0: Discoverable, 1: NonDiscoverable */
METADATAVERSION='1' /* default start number is 1 */
VIDEO_TV='2' /* 1: NTSC, 2: PAL */
VIDEO_SOURCE1='0,user0,0,0,0,0,720,576'
VIDEO_ENCODER1='HighResolution_MPEG4,HighResolution MPEG4,0,1,720,576,80,0,0,0,0,0,0,PT0S'
VIDEO_ENCODER2='VGA_MPEG4,VGA MPEG4,0,1,640,480,80,0,0,0,0,0,0,PT0S'
VIDEO_ENCODER3='HighResolution_JPEG,HighResolution JPEG,0,0,720,576,80,0,0,0,0,0,0,PT0S'
VIDEO_ENCODER4='VGA_JPEG,VGA JPEG,0,0,640,480,80,0,0,0,0,0,0,PT0S'
VIDEO_ENCODER5='0,user0,0,1,720,576,80,0,0,0,0,0,0,PT0S'
VIDEO_ENCODER6='1,user1,0,1,720,576,80,0,0,0,0,0,0,PT0S'
MEDIA_PROFILE1='1,HighResolution_MPEG4,HighResolution MPEG4,0,0'
MEDIA_PROFILE2='1,VGA_MPEG4,VGA MPEG4,0,1'
MEDIA_PROFILE3='1,HighResolution_JPEG,HighResolution JPEG,0,2'
MEDIA_PROFILE4='1,VGA_JPEG,VGA JPEG,0,3'
SCOPES='0,onvif://www.onvif.org/type/video_encoder'
SCOPES='0,onvif://www.onvif.org/type/audio_encoder'
SCOPES='0,onvif://www.onvif.org/hardware/'
SCOPES='0,onvif://www.onvif.org/name/ACD2100'
SCOPES='1,onvif://www.onvif.org/location/'
SCOPE_LOCATION_COUNT='1'

## Slide 9
/etc/default/default.conf
  Please add:
    ONVIF_ENABLED= '0' ## 0:disabled, 1:enabled
Rule.make
  Please add macro identifier (#define) “HAVE_ONVIF”. For example:
    CFLAGS += -DHAVE_ONVIF

## Slide 10
SVN
https://vcs-subversion.acti.com/
svn/SSPO/CommonLibs/Gsoap/
generate libsoap.a
Needed by the
Libsoap.a & firmware Server.
Needed by firmware Server

## Slide 11: Example
Implement ONVIF function
int __trt__GetXYZ(struct soap *soap, struct _trt__GetXYZ *trt__GetXYZ, \
struct _trt__GetXYZResponse *trt__GetXYZResponse)
{
  trt__GetXYZResponse->ABC = (struct tt__ABC *)soap_malloc(soap, sizeof(struct tt__ABC));
  soap_default_tt__ABC(soap, trt__GetXYZResponse->ABC);
  …
  …
  …
  …
  return SOAP_OK;
}

## Slide 12: Non-implemented
Device Management
  SetDynamicDNS, GetDynamicDNS
  GetAccessPolicy, SetAccessPolicy
  GetCertificates, GetCertificatesStatus, SetCertificatesStatus, DeleteCertificates, GetPkcs10Request, LoadCertificates, GetClientCertificateMode, SetClientCertificateMode
  GetUsers, SetUser, CreateUsers, DeleteUsers
  SetRelayOutputSettings
Media Configuration
  GetAudioSources, AddAudioEncoderConfiguration, AddAudioSourceConfiguration, RemoveAudioEncoderConfiguration, RemoveAudioSourceConfiguration, GetAudioSourceConfigurations, GetAudioEncoderConfigurations, GetAudioSourceConfiguration, GetAudioEncoderConfiguration, GetCompatibleAudioEncoderConfigurations, GetCompatibleAudioSourceConfigurations, SetAudioSourceConfiguration, SetAudioEncoderConfiguration, GetAudioSourceConfigurationOptions, GetAudioEncoderConfigurationOptions
If the NVT supports dynamic DNS as specified
in [RFC 2136] and [RFC 4702], it MUST be
possible to get or set the type, name and TTL through the GetDynamicDNS or SetDynamicDNS command.

## Slide 13: How to integrate various Platforms?
Import Config library
Add Gsoap library
Review all functions